Total cost under 5K€
Automatic calibration procedure.
Airspeeds from 5 m/s up to 40m/s (18km/h up to 144 km/h)
Airspeed accuracy calibration uncertainty 0,5% or less; at full scale 0.2m/s.
Altitude 0 to 5000 MSL
Altitude accuracy 0.8m.
Total pressure 95460 Pa to 102305 Pa
Static pressure 101325 Pa to 95460 Pa
Sensors should have a sample rate > 20 Hz; Average of multiple measurements will be use.
Battery powered + plug powered
Able to read temperature from a remote digital temperature probe; 1°C accuracy or better. Range -10°C to 50°C.
Able to manage communication with a PC for log purposes.
That piece of hardware should be able to calibrate and test vertical speed indicators?